## Slide 1: Application taxonomy & characterization
Paul Grun
Cray Inc.
Dec 17, 2013

## Slide 2: OFWG objective
Deliver (an) I/O stack(s) that maximize(s) application effectiveness
To do that, we need to understand how applications use I/O
But what “applications”?

## Slide 3: Today’s objective
Begin to develop a taxonomy for classes of applications to help us focus on defining the requirements that characterize a given class
Understand the dimensions in which an application’s I/O characteristics are described

## Slide 4: Framework
Fabric Interfaces
Fabric Provider Implementation
I/O service
I/O service
I/O service
…
Application(s)
We have begun to develop an idea about what the framework might look like
Next step is to understand application requirements to guide API development
Message Queue
Control
Interface
RDMA
Atomics
Active Messaging
Tag Matching
Collective Operations
CM Services

## Slide 5: Characterizing applications
Fabric Interfaces
Fabric Provider Implementation
I/O service
I/O service
I/O service
…
Application(s)
Provider layer defines a set of I/O services. (We do not define how the service is provided (s/w? h/w?), only that it exists)
Fabric interface layer exposes the services defined by the provider layer
Ultimate objective is to characterize application I/O requirements in terms of a set of proposed I/O services
Message Queue
Control
Interface
RDMA
Atomics
Active Messaging
Tag Matching
Collective Operations
CM Services

## Slide 6: I/O Characteristics
Sided-ness – single ended or double ended operations
Strided transfers
Memory protection & isolation requirements
Transmission ordering requirements
Data placement ordering requirements
Data delivery ordering requirements
Caching and memory locality
Interrupts - control over CPU affinity
Reliability requirements
Signaling requirements
Transfer size requirements
Latency requirements – is latency important
Bandwidth requirements – is bandwidth important
Synchronous operations
Asynchronous operations
Synchronization operations – atomics, immed data…
Connection services – connected, unconnected
Shared resources – is there a requirement for multiple processes to share an object
Variably sized memory resource requirements – ability to minimize memory footprint
Transmission distance
Multi-pathing requirements
High availability
Fork support
Proper registration support – MPI support

## Slide 7: OFS application support
SA | Subnet Administrator
MAD | Management Datagram
SMA | Subnet Manager Agent
PMA | Performance Manager Agent
IPoIB | IP over InfiniBand
SDP | Sockets Direct Protocol
SRP | SCSI RDMA Protocol (Initiator)
iSER | iSCSI RDMA Protocol (Initiator)
RDS | Reliable Datagram Service
UDAPL | User Direct Access Programming Lib
HCA | Host Channel Adapter
R-NIC | RDMA NIC
Common
InfiniBand
iWARP
Key
InfiniBand HCA
iWARP R-NIC
Hardware
Specific Driver
Hardware Specific
Driver
Connection Manager
MAD
InfiniBand OpenFabrics Kernel Level Verbs / API iWARP R-NIC
SA Client
Connection
Manager
Connection Manager
Abstraction (CMA)
InfiniBand OpenFabrics User Level Verbs / API iWARP R-NIC
SDP
IPoIB
SRP
iSER
RDS
SDP Lib
User Level MAD API
Open SM
Diag
Tools
Hardware
Provider
Mid-Layer
Upper Layer Protocol
User APIs
Kernel Space
User Space
NFS-RDMA
RPC
Cluster
File Sys
Application Level
SMA
Clustered
DB Access
Sockets
Based Access
Various
MPIs
Access to
File
Systems
Block
Storage
Access
IP Based
App
Access
Apps & Access Methods for using OF Stack
UDAPL
Kernel bypass
Kernel bypass
Connection Manager

## Slide 8: OFS application support - today
Clustered
DB Access
Various
MPIs
File
Systems Access
Block
Storage
Access
IP-based
and
Sockets-based apps
Support for various types of legacy apps
Distributed computing via message passing
Network-attached block storage
Extracting value from structured data
Network-attached file or object storage

## Slide 9: OFS application support
Legacy apps (skts, IP)
Data Analysis
Data Storage, Data Access
Filesystems
Object storage
Block storage
Structured data
Skts apps
IP apps
The ways that data is organized, so value can be extracted.
The ways that users store and access data, and the ways that users collaborate through data.
Programming models for processing data
Distributed Computing
Message Passing
- MPI applications
Clustered
DB
Various
MPIs
File
Systems
Block
Storage
IP, skts apps

## Slide 10: Broadening support
Legacy apps (skts, IP)
Data Analysis
Data Storage, Data Access
Structured data
Unstructured data
Skts apps
IP apps
Add to the Data Analysis category:
- Unstructured data, because people want to extract value from avalanches of unorganized data. (which is the essence of Big Data).
Hadoop, for example.
What are the I/O requirements to support tools for accessing and analyzing both structured and unstructured data?
Filesystems
Object storage
Block storage
Distributed Computing
Via msg passing
MPI applications
Distributed Computing

## Slide 11: Broadening support
Legacy apps (skts, IP)
Data Analysis
Data Storage, Data Access
Structured data
Unstructured data
Skts apps
IP apps
Distributed storage because of the shift in how data is accessed (e.g. from anywhere)  Cloud storage
Storage at a distance because distributed teams of users demand the ability to collaborate through common, shared data
Same question – what are the I/O requirements to support data storage and access?
Distributed Computing
Via msg passing
MPI applications
Filesystems
Object storage
Block storage
Distributed storage
Storage at a distance

## Slide 12: Broadening support
Legacy apps (skts, IP)
Data Analysis
Data Storage, Data Access
Distributed Computing
Filesystems
Object storage
Block storage
Distributed storage
Storage at a distance
Message passing
MPI applications
Structured data
Unstructured data
Skts apps
IP apps
Support for Distributed Computing – improved support for MPI
(Yes, we already have PSM (and MXM) to address this.)
Can we improve the scalability of message passing programming models?

## Slide 13: Broadening support
Legacy apps (skts, IP)
Data Analysis
Data Storage, Data Access
Distributed Computing
Filesystems
Object storage
Block storage
Distributed storage
Storage at a distance
Message passing
MPI applications
Structured data
Unstructured data
Skts apps
IP apps
Support for Distributed Computing
Add support for shared memory programming models
Shared memory
- PGAS languages

## Slide 14: MP vs shared memory
There are endless debates over the value of one vs the other.
Some say you can implement shared memory over a MP architecture, and some say the reverse.
The question is not message passing VS shared memory.
Rather than debate the merits, we could discuss:
Where does a message passing architecture make sense and how can it be improved?
Should OFS improve its support for shared memory models (e.g. PGAS), and if so, how?

## Slide 15: Expanded taxonomy
Legacy apps (skts, IP)
Data Analysis
Data Storage, Data Access
Distributed Computing
Filesystems
Object storage
Block storage
Distributed storage
Storage at a distance
Via msg passing
MPI applications
Structured data
Unstructured data
Skts apps
IP apps
Via shared memory
- PGAS languages

## Slide 16: Expanded taxonomy
Legacy apps (skts, IP)
Data Analysis
Data Storage, Data Access
Distributed Computing
Filesystems
Object storage
Block storage
Distributed storage
Storage at a distance
Via msg passing
MPI applications
Structured data
Unstructured data
Skts apps
IP apps
Via shared memory
- PGAS languages
Probably the critical three?
Reasonably good representation in current OFWG
Some hope of finding representation
??

## Slide 17: Next steps
Decide on an appropriate taxonomy to describe applications
Agree on the appropriate set of I/O characteristics to be used to characterize an application
For each class of application, identify interested parties capable of proposing a characterization for that class