## Slide 1: Windows RDMA File Storage
Tom Talpey, Microsoft
Filesystems Panel track

## Slide 2: SMB3
The primary Windows remote file protocol
Long SMB history, since 1980’s
  SMB1 since Windows 2000 (“CIFS” before that)
  SMB2.0 with Vista and Windows Server 2008, 2.1 in 7/2008R2
Now at dialect 3
  SMB3.0 with Windows 8/Server 2012, SMB3.02 in 8.1/WS2012R2
Supported:
  Full Windows File API
  Enterprise applications
  Hyper-V Virtual Hard Disks
  SQL Server
  New in Windows Server 2012 R2:
    Hyper-V Live Migration
    Shared VHDX - Remote Shared Virtual Disk MS-RSVD

## Slide 3: SMB3 Features
Connection management
  Dialect negotiation, validation
Authentication
  Integrity (signing) and/or privacy (encryption)
Multichannel
  Provides both trunking/bandwidth and availability
Resilience and recovery to network failure
RDMA (in Windows Server)
File I/O semantics (Win32, and others)
  With control and extension semantics
  Filesystem and IOCTL passthrough
Remote access
  NTFS, VHD, Named Pipes, RPC, Memory, …
Notes: In practice, a Session layer as well as a remote filesystem

## Slide 4: SMB Direct (RDMA)
Transport layer protocol adapting SMB3 to RDMA
Fabric agnostic
  iWARP, InfiniBand, RoCE
  IP addressing
    IANA registered (smbdirect 5445)
Minimal provider requirements
  Enables greatest compatibility and future adoption
  Only send/receive/RDMA Write/RDMA Read
  RC-style, no atomics, no immediate, etc.
Supported inbox in WS2012 and WS2012R2:
  iWARP (Intel and Chelsio RNICs at 10 and 40GbE)
  RoCE (Mellanox HCAs at 10 and 40GbE)
  InfiniBand (Mellanox HCAs at up to FDR 54Gb)

## Slide 5: SMB Multichannel
Full Throughput
Bandwidth aggregation with multiple NICs
Multiple CPUs cores engaged when NIC offers Receive Side Scaling (RSS) or RDMA used – NUMA-aware
Automatic Failover
SMB Multichannel implements end-to-end failure detection
Leverages NIC teaming (LBFO) if present, but does not require it
Automatic Configuration
SMB detects and uses multiple paths
Zero-config – simply install adapters
Sample Configurations
Multiple RDMA NICs
Multiple 1GbE NICs
Single 10GbE RSS-capable NIC
SMB Server
SMB Client
SMB Server
SMB Client
SMB Server
SMB Client
Multiple 10GbE in LBFO team
SMB Server
SMB Client
LBFO
LBFO
Switch
10GbE
NIC
10GbE
NIC
10GbE
Switch
10GbE
NIC
10GbE
NIC
10GbE
NIC
10GbE
NIC
10GbE
Switch
1GbE
NIC
1GbE
NIC
1GbE
Switch
1GbE
NIC
1GbE
NIC
1GbE
Vertical lines are logical channels, not cables
Switch
10GbE/IB
NIC
10GbE/IB
NIC
10GbE/IB
Switch
10GbE/IB
NIC
10GbE/IB
NIC
10GbE/IB
Switch
10GbE

## Slide 6: Performance
Key file I/O workloads
  Small/random – 8KB, IOPS sensitive
  Large/sequential – 512KB, bandwidth sensitive
  Smaller, and larger (up to 8MB), are also relevant
Multichannel achieves higher scaling
  Bandwidth and IOPS from additional network interfaces
  Affinity and parallelism in endnodes
Unbuffered i/o allows zero-touch to user buffer
Strict memory register/invalidate per-I/O
  Key to enterprise application integrity
  Performance maintained with remote invalidate and careful local behaviors

## Slide 7: Performance
Workload | IOPs
8KB reads, mirrored space (disk) | ~600,000
8KB reads, from cache (RAM) | ~1,000,000
32KB reads, mirrored space (disk) | ~500,000
Throughput >16 Gbytes/second 45% better than Windows Server 2012 Larger I/Os (>32KB) – similar results, i.e. larger i/o is not needed for achieving full performance! | 
File Server
(SMB 3.0)
File Client (SMB 3.0)
SQLIO
RDMA NIC
RDMA NIC
RDMA NIC
RDMA NIC
RDMA NIC
RDMA NIC
SAS
SAS HBA
JBOD
SSD
SSD
SSD
SSD
SSD
SSD
SSD
SSD
SAS
SAS HBA
JBOD
SSD
SSD
SSD
SSD
SSD
SSD
SSD
SSD
SAS
SAS HBA
JBOD
SSD
SSD
SSD
SSD
SSD
SSD
SSD
SSD
SAS
SAS HBA
JBOD
SSD
SSD
SSD
SSD
SSD
SSD
SSD
SSD
SAS
SAS HBA
JBOD
SSD
SSD
SSD
SSD
SSD
SSD
SSD
SSD
Storage Spaces
SAS
SAS HBA
JBOD
SSD
SSD
SSD
SSD
SSD
SSD
SSD
SSD
Link to full demo in “Resources” slide below
Single client, single server, 3xIB FDR multichannel connection, to storage and to RAM

## Slide 8: Resources
Jose Barreto’s blog
  http://smb3.info/
  The Rosetta Stone: Updated Links on Windows Server 2012 R2 File Server and SMB 3.02
    http://blogs.technet.com/b/josebda/archive/2014/03/30/updated-links-on-windows-server-2012-r2-file-server-and-smb-3-0.aspx
  Performance Demo
    http://blogs.technet.com/b/josebda/archive/2014/03/09/smb-direct-and-rdma-performance-demo-from-teched-includes-summary-powershell-scripts-and-links.aspx
SNIA Storage Developer’s Conference
  SDC presentations (multiple years, SMB track)
    http://www.snia.org/events/storage-developer/archive
Protocol documentation
  Microsoft Open Specifications
    http://www.Microsoft.com/protocols
  [MS-SMB2]: Server Message Block (SMB) Protocol Versions 2 and 3
    http://msdn.microsoft.com/en-us/library/cc246482.aspx
  [MS-SMBD]: SMB2 Remote Direct Memory Access (RDMA) Transport Protocol
    http://msdn.microsoft.com/en-us/library/hh536346.aspx
Microsoft Technet
  Improve Performance of a File Server with SMB Direct
    http://technet.microsoft.com/en-us/library/jj134210.aspx
Windows Kernel RDMA interface
  NDKPI Reference (provider)
    http://msdn.microsoft.com/en-us/library/windows/hardware/jj206456.aspx

## Slide 9: Thank You