## Slide 1: iWARP Update
#OFADevWorkshop

## Slide 2: Increasing interest in iWARP
RDMA Use Cases
  High Performance Computing
  File and Block Storage
  NVM access
  Virtual Machine migration
  Low-latency messaging middleware
  Virtualization and Cloud deployments place important requirements on these use cases
Key iWARP value propositions for these use cases
  Engineered for “typical” Ethernet (best effort, no DCB, no QCN, etc)
  Natively Routable
  Multi-pathing supported at Layer 3 (as well as Layer 2)
  Reliable and proven TCP Transport
    Mature and efficient retransmission algorithms
    Dynamic and verified congestion algorithms

## Slide 3: iWARP Standards
iWARP updates and enhancements are handled by the IETF STORM (Storage Maintenance) working group
Finalized RFCs
  RFC 5040 A Remote Direct Memory Access Protocol Specification
  RFC 5041 Direct Data Placement over Reliable Transports
  RFC 5044 Marker PDU Aligned Framing for TCP Specification
  RFC 6580 IANA Registries for the RDDP Protocols
  RFC 6581 Enhanced RDMA Connection Establishment
3
Notes: 2007 - 5040, 5041, 5044
2012 - 6580, 6581
RFC 6581
Extends RFCs 5043 and 5044
Original iWARP did not have a concept of RTR state exit
  Assumed active side of connection sent first RDMA message
Application was responsible for ORD/IRD negotiation
  Typically used application messages or private data
iWARP connection establishment enhancements:
  Ready to Receive (RTR) Message Negotiation
  Standardized ORD/IRD Negotiation

## Slide 4: iWARP In-Progress RFCs
draft-ietf-storm-rdmap-ext-09.txt
  Extends RFC 5040
    Adds Atomic Operations and Immediate Data
  Authors from Intel, Broadcom, Chelsio
  IESG approved. Next step RFC Editor Queue
draft-ietf-wood-rdmap-ext-v2-00.txt
  Extends RFC 5040
    Add Send with Immediate Data
    Add IB-style RDMA Read
  Authors from Intel
  Submitted for initial review by STORM working group
4

## Slide 5: Traditional iWARP RDMA Read
RDMA NIC
SQ WQE
RDMA Read op
STag describing Sink buffer
STag describing Source buffer
Sink Buffer
RDMA Read Request message with
STag describing Source buffer and
STag describing Sink buffer
Source
Buffer
RDMA NIC
DMA
Read
RDMA Read Response with Data and
STag describing Sink buffer
DMA Write
SQ WQE
Local Invlidate op
STag describing Sink buffer
This slide has animations – view in Presentation mode
5

## Slide 6: IB-style RDMA Read
Source
Buffer
RDMA NIC
SQ WQE
RDMA Read op
SGL describing Sink buffers
R_Key or STag describing Source buffer
Sink Buffer
Sink Buffer
Sink Buffer
…
RDMA Read Request message with
R_Key or STag describing Source buffer
RDMA NIC
RDMA Read Response with Data
DMA Writes
DMA
Read
No Sink Buffer Local Invalidate required, because Sink buffer R_Key (STag) not exposed to network
This slide has animations – view in Presentation mode
In-progress RFCs enable this flow on iWARP
6

## Slide 7: Goal of In-Progress RFCs
Common Application capabilities across all flavors of RDMA
These RFCs remove all known application differences between iWARP and InfiniBand

## Slide 8: IETF Alignment/Synergy with iWARP
iWARP currently leverages:
  TCP
    Reliable transport and congestion management
  Explicit Congestion Notification
    Inherited from TCP/IP layers
iWARP will naturally adopt/use:
  Tunneling/Network Overlays
    iWARP works with (but does not require) existing tunnel protocols (ie Generic Routing Encapsulation) and NVO3 technology investigations
Connectionless messaging to complement iWARP RDMA
  Typically realized with unreliable datagrams (unicast and multicast)
  InfiniBand has Unreliable Datagram (UD)
  UDP may be used in place of UD for Ethernet implementations
    No new wire protocol standards required

## Slide 9: iWARP Ecosystem
Strong industry support to evolve iWARP
Good alignment with IETF, and support in STORM to evolve the standards
OFED 3.5-2 stable drivers from multiple vendors: cxgb3, cxgb4, nes
Intel is implementing iWARP RDMA as a key capability in Fort Park. Fort Park is an Ethernet IP block that will be integrated into future Intel server chipsets.
Notes: http://www.openfabrics.org/downloads/OFED/release_notes/OFED_3.5-2_release_notes.txt

## Slide 10: Call to Action
Participate in STORM standards reviews
iWARP RNIC vendors and system software vendors consider supporting the in-progress RFCs as soon as possible
Develop future RDMA extensions with a goal to enable them across all flavors of RDMA
Notes: http://www.openfabrics.org/downloads/OFED/release_notes/OFED_3.5-2_release_notes.txt

## Slide 11: Thank You