## Slide 1: RDMA Bonding
Liran Liss
Mellanox Technologies

## Slide 2: Agenda
Introduction
Transport-level bonding
RDMA bonding design
Recovering from failure
Implementation

## Slide 3: Bonding (Link Aggregation)
Bond together multiple physical links into a single aggregate logical link
Motivation
  Aggregate bandwidth (active-active)
    Distribute communication flows across all active links
  High availability (active-backup)
    If a link goes down, reassign traffic to remaining links
Can we do the same for HCAs?

## Slide 4: Link-level Bonding
Example: Ethernet link aggregation
Typically accomplished by a “Bonding” pseudo network interface
Placed between the L3/4 stack and physical interfaces
  Multiplexes packets across stateless network interfaces
  Transparent to higher levels of the stack
  Transport is implemented in SW
RDMA challenge
  Transport implemented at stateful network interfaces (HCAs)
netdev1
netdev2
Bonding
IP
TCP
UDP
Sockets
Application
subnet1
Packets

## Slide 5: Session-level Bonding
Example: iSCSI
Initiator establishes a session with Target
  Session may comprise multiple TCP flows
Connections are completely encapsulated within the iSCSI session
  OS issues SCSI commands
Alternatively, multiple sessions may be created to the same target/LUN
  May be presented as single logical LUN by multi-path SW
RDMA challenge
  Transport connections visible to ULPs
  Multiple RDMA consumers
SCSI subsystem
iSCSI HBA
I-T Session
TCP1
TCP2
netdev1
netdev2
SCSI CMDs
subnet1

## Slide 6: Idea: Transport-level Bonding
Provided by a pseudo-HCA (vHCA)
Applications open virtual resources
  vPDs, vQPs, vSRQs, vCQs, vMRs
  Mapped to physical resources by vHCA
Namespace translated on the fly
  Similar to transparent RDMA migration
    IBM/OSU “Nomad” paper
    VMware vRDMA
    Oracle live-migration prototype
Link aggregation
  Distribute QPs across HCAs
  Optionally bond different HCA types
  Upon failover
    Reconnect over a different device/port
    Continue traffic from the point of failure
  Transparent migration is a special HA case
subnet2
subnet1
RDMA HAL and services
Application
IB HCA
RoCE HCA
Bonding HCA driver
Verbs
Notes: HA is substantially different that just migration

## Slide 7: Requirements
Support aggregate across different physical HCAs
  Optionally even different device types
HW independent Bonding driver
Strict semantics
  Adhere to transport message ordering guarantees
  Global visibility of all IO operations
Transparent to consumers
  Including failover events
High performance

## Slide 8: Design
User-space solution
  Bond driver is a Verbs provider
  Uses RDMACM internally
    To open connections
    Negotiate state using private data
IP addressing
  GID = IP
  QPN = Port number
  HCA identity = alias IP
1:1 virtualphysical QP mapping
  Leverage HW ordering guarantees
  Zero copy messages
Fast path done in app context
  Post_Send(), Post_Recv(), PollCQ()
Vendor driver2
libibvers
Vendor driver1
RDMA bond
Kernel drivers
rdmacm
Application
U
K

## Slide 9: Object Relations (Example)
RDMA Bond
vMR1
vPD1
HCA2
PD24
QP9
vQP1
vRQ
Connection
RDMA ID
Listener
RDMA ID
MR2
HCA1
PD83
CQ69
MR2
vSQ
vMR2
vQP2
vRQ
Connection
RDMA ID
Listener
RDMA ID
vSQ
QP3
CQ17
vCQ1
vRKey | RKey
1 | 635
2 | 145
vRKey | RKey
1 | 201
2 | 36

## Slide 10: Posting WRs
If vQP is not in a suitable state or virtual queue is full
  Return immediate error
Enqueue WR in virtual Queue
If associated HW Send / Receive queue is full
  Return with success
For Sends
  If connection is not active
    Schedule (re)connection and return with success
  For UD
    Resolve AH and remote QPN (if not already cached)
  For RDMA
    Resolve RKey (if not already cached)
For Receives
  If connection is not active, return with success
Translate local SGE
Post to HW

## Slide 11: Polling Completions
Poll next HW CQ associated with vCQ
If not empty, process according to status
  Case IBV_WC_RETRY_EXC_ERR
    Schedule reconnection for associated vQP
    Ignore completion
  Case IBV_WC_WR_FLUSH_ERR
    Ignore completion
  Case IBV_WC_SUCCESS
    Report successful completion
  Default (any other error)
    Modify vQP to error
    Report erroneous completion
    Add corresponding virtual Queue to CQ error list
Poll next virtual queue on error list
If it has in-flight WQEs
  Generate ERROR_FLUSH for next WQE
Report CQ empty if none of the above applies

## Slide 12: RC Failure Recovery
Re-establish connection
  Over any active link and device
Negotiate last committed operations
  Generate corresponding completions
Rewind physical queues
  Resume operation
Send Queue
Receive
Queue
virtual producer
Virtual
consumer
Physical
producer
virtual producer
Virtual
consumer
Physical
producer

## Slide 13: RC Failure Recovery
Send Queue
Receive
Queue
virtual producer
Virtual
consumer
Physical
producer
virtual producer
Virtual
consumer
Physical
producer
Re-establish connection
  Over any active link and device
Negotiate last committed operations
  Generate corresponding completions
Rewind physical queues
  Resume operation

## Slide 14: RC Failure Recovery
Send Queue
Receive
Queue
virtual producer
Virtual
consumer
virtual producer
Virtual
consumer
Re-establish connection
  Over any active link and device
Negotiate last committed operations
  Generate corresponding completions
Rewind physical queues
  Resume operation

## Slide 15: RC Failure Recovery
Send Queue
Receive
Queue
virtual producer
Virtual
consumer
virtual producer
Virtual
consumer
Re-establish connection
  Over any active link and device
Negotiate last committed operations
  Generate corresponding completions
Rewind physical queues
  Resume operation

## Slide 16: RC Failure Recovery
Send Queue
Receive
Queue
virtual producer
Virtual
consumer
Physical
producer
virtual producer
Virtual
consumer
Physical
producer
Re-establish connection
  Over any active link and device
Negotiate last committed operations
  Generate corresponding completions
Rewind physical queues
  Resume operation

## Slide 17: Implementation (Ongoing)
Current status
  POC implementation
  Supported objects
    CQs
    PDs
    RC QPs
    MRs
  Supported operations
    Resource manipulation
    Send-receive data traffic
  QPs limited to single link
    Tackle transient link failure
Next steps
  Complete Verbs coverage
  RDMACM integration
  Multi-link recovery
    Continuously negotiate active links
  Aggregation schemes
    HA
    RR
    Static load balancing
    Dynamic load balancing

## Slide 18: Summary
Bonding solution for stateful RDMA devices
  HW agnostic
  Aggregates ports from different devices
  Communicating peers must run the Bonding driver
    Out-of-band protocol via CM MADs
Supports
  High availability
  Aggregate BW
  Load balancing
  Transparent migration
Efficient user-space implementation
  Could be extended to the kernel in a similar manner

## Slide 19: Thank You